| Emergency |
| --- |
| Engine Failure |
| Airspeed - Best glide | 80 KIAS |
| Pick landing location | Into wind |
| Mixture | Full In (Rich) |
| Alternate Air | Pull and leave it Pulled |
| Magnetos | Check |
| Fuel Selector | Fullest Tank |
| Ignition | Both or Start |
| Flaps | As Required |
| Emergency Frequency | 121.5 |
| Emergency Squawk Code | 7700 |
| Master switch | Off |
| Cabin Doors | Unlatch |
| Touchdown | Tail Low |
| Emergency Descent |
| Throttle | Idle |
| Mixture | Full In (Rich) |
| Propeller | Full In (High RPM) |
| Flaps | Full |
| Bank at 45 Deg |  |
| Descend at V(FE) | 87 KIAS |
| Fire during Start Up |
| Starter | Continue Cranking |
| Mixture | Full Out (Lean) |
| Throttle | Full In (Open) |
| Fuel Selector | Off |
| Fire In Flight |
| Fuel Selector | Off |
| Throttle | Full Out (Idle) |
| Mixture | Full Out (Lean) |
| Fire Extinguisher | Undo Clasp and pull Pin |
| Fire - Electrical |
| Master Switch | Off |
| Vents | Open |
| Cabin Heat | Off |
| Radio failure / Light Signals |
| If Tower Controlled, Squawk 7600, Pattern + 500 ft. |
| Steady Green | Clear to Land / Takeoff |
| Flashing Green | Return to Land |
| Steady Red | Giveway to Aircraft |
| Flashing Red | Unsafe / Clear Runway |
| Flashing White | Return to Starting Point |
| Flashing Red / Green | Warning - Caution |
| N519RV (Van’s RV-10) Airspeeds (KIAS) |
| Vs0 58 | Vfe 87 |
| Vs1 63 | Va 107 |
| Vx 80 | Vno 160 |
| Vy 80 | Vne 200 |
| Kansas City Approach (Class B) Frequencies |
| 118.9 - South of LWC Apt. | 124.7 – West of MCI Rwy 01/19 |
| 119.0 – East of MCI Rwy 01/19 |  |
| 1-800-WX-BRIEF | 1-800-992-7433 |
| N519RV (Van’s RV-10 ) - Preflight |
| Cockpit Pre-Flight Inspection |
| Aircraft Docs (ARROW) | Check |
| Weight & Balance | Check |
| Ignition | Off |
| All Switches | Off |
| Master Switch | On (Battery Position) |
| Avionics Main Switch | On |
| Left and Right Fuel Gauge | Check |
| Fuel Remaining on EMS | Adjust if Fuel Added |
| Trip Timer on EMS | Reset when Fully Fueled |
| Flaps | Extend |
| Master & Avionics Main Switch | Off |
| Pitot Heat (if required) | Test for Heat |
| Windows | Clean |
| Fuselage and Empennage Pre-Flight Inspection |
| Baggage Door and Lock | Check |
| Static Ports | Check |
| Control Surfaces | Free and Secure |
| Tie Down | Disconnect |
| Trim Tab | Check security |
| Antennas | Check security |
| Nav/Strobe Lights | Check Lens and Lamps |
| Rudder/Trim Cables | Check |
| Right Wing Pre-Flight Inspection |
| Flaps | Secure |
| Aileron | Free and Secure |
| Nav/Landing/Strobe Lights | Check Lens and Lamps |
| Tie Down | Disconnect and Remove |
| Fuel Quantity | Visually Check |
| Fuel Filler Cap | Secure |
| Main Wheel | Condition and Inflated to 40 PSI |
| Brakes | Check Pads and Lines for Leaks |
| Fuel Tank Sump | Sample |
| Fuel Tank Vent | Check |
| Firewall Forward Pre-Flight Inspection |
| Nose Wheel | Condition and Inflated to 38 PSI |
| Prop & Spinner | Check |
| Alternator Belt | Check |
| Air Intake, Filter & Prop Cable | Check |
| Engine Oil Level | Check (Run at 9 Qt, Add at 8 Qt) |
| Hinge Pins | Check and Secure |
| Left Wing Pre-Flight Inspection |
| Main Wheel | Condition and Inflated to 40 PSI |
| Brakes | Check Pads and Lines for Leaks |
| Fuel Tank Sump | Sample |
| Fuel Tank Vent | Check |
| Fuel Quantity | Check |
| Fuel Filler Cap | Secure |
| Pitot Tube | Uncover and Check |
| Tie Down | Disconnect and Remove |
| Nav/Taxi/Strobe Lights | Check Lens and Lamps |
| Aileron | Free and Secure |
| Flaps | Secure |
| Ground Procedures |
| Before Starting Engine |
| Preflight Inspection | Complete |
| Engine Controls | Free |
| Fuel Selector | Fullest/Desired Tank |
| Seats Belts | On/Adjusted |
| Main & Aux Avionics Switches | Off |
| Parking Brake & Brakes | Parking Brake (Release), Brakes (Set) |
| Engine Starting and Run Up |
| Master Switch | On (Battery Position) |
| Flaps | Full Up |
| Alternate Air | Full In (Don’t pull on the Ground) |
| Propeller | Full In (High RPM) |
| Cold Start |  |
| Mixture | Full In (Rich) |
| Throttle | 1/8 Inch |
| Boost Pump | Run till you hear the Pressure Build |
| Hot Start |  |
| Mixture | Full Out until it fires then Full In |
| Throttle | 1/8 Inch |
| Boost Pump | On once Mixture Full In, then Off |
| Propeller Area | Clear |
| Ignition | Start |
| Throttle | Adjust to 1000 - 1200 RPM |
| Master Switch | On (Alternator Position) |
| Main & Aux Avionics Switch | On |
| Oil Pressure | Check |
| Ammeter | Charging (Positive Value) |
| Voltmeter | +14 Volts |
| EFIS Altimeter and Altimeter | Set for Field Elevation (+/- 75 Ft) |
| ATIS/AWOS/ASOS | Obtain |
| Cabin Doors | Closed & Locked (Check Door/Frame Gap) |
| Seats Belts | Adjust & Lock |
| Flight Controls | Free & Correct |
| Elevator Trim | Takeoff Position |
| Throttle Setting | 2000 rpm |
| Magnetos | Check |
| Propeller | Cycle (500 rpm drop) |
| Engine Instruments | Check |
| Mixture | Lean (Out 1”) for Taxi |
| Radio/Nav Equipment | Setup desired Freq and Nav Points |
| Transponder | VFR(1200) or Squawk Code |
| Nav Lights | On for Night Flying |
| Strobe Lights | On |
| Taxi/Landing Light | On for Night Takeoff |
| Wig-Wag Lights | On (Off if Taxi/Landing Light is Used) |
| Pitot Heat | As Required |
| Before Takeoff |
| Fuel Selector | Fullest/Desired Tank |
| Boost Pump | On (Off once 1000 AGL) |
| Mixture | Full In (Rich) |
| In-Flight / Post Flight |
| Takeoff |
| Flaps | Full Up |
| Power | Full Throttle (Prop Full In) |
| Elevator | Lift at 60 KIAS |
| Climb ( > 1000 Feet AGL) | 110 KIAS (25” @ 2500 RPM) |
| Cruise |
| Set Desired Power | 20 to 24.5 Squared |
| Mixture | 25 – 75 lean of Peak if < 75% Pwr |
| EGT | < 1500 degrees F |
| CHT | < 425 degrees F |
| Engine Instruments | Scan |
| Before Landing |
| Mixture | Full In (Rich) |
| Boost Pump | On |
| Propeller | Full In (High RPM) if < 80 KIAS |
| Flaps (below 87 KIAS) | Half or Full (As Desired) |
| Approach Speed | 70 - 80 KIAS (Load Dependent) |
| After Landing |
| Flaps | Full Up |
| Mixture | Lean 1" for Taxi |
| Boost Pump | Off |
| Transponder | Standby (Check) |
| All Lights | As Required |
| Shutdown / Parking |
| Throttle | 1000 RPM |
| Flight Time | Record from EMS |
| All Switches | Off (from Right to Left) |
| Mixture | Full Lean |
| Ignition / Magnetos | Off (Remove Key) |
| CLOSE FLIGHT PLAN | CLOSE FLIGHT PLAN |
| Securing the Aircraft |
| Parking Brake | Set |
| Stick Controls | Secure with Seat Belt |
| Rudder | Secure |
| Cabin Doors | Secure |
| Pitot Tube | Cover |
| Tie Downs | Install and Secure |
| Chocks | Install |
| Nearby Airports |
| Johnson Cnty Exec - OJC | New Century – IXD |
| 18-36 1096 ft. | 17-35 & 04-22 1087 ft. |
| Tower 126.0 | Tower 133.0 |
| Ground 121.6 | Ground 124.3 |
| VOR 113.0 | AWOS 135.325 |
| ATIS 119.35 |  |
| Gardner - K34 | Miami Co. - K81 |
| 03-21, 08-26, & 17-35 | 03-21 940 ft. |
| Elev 1042 ft. | CTAF 122.8 |
| CTAF 122.8 |  |